## Slide 1: Distributed control solutions for DER integration
Jakob stoustrup
Professor, PhD
jakob@es.aau.dk

## Slide 2: Distributed Control for Grid Applications
Applications of distributed control for grid
  Frequency control through optimal load management
  Multi-agent based load shedding
  Distributed economic dispatch
  Economic AGC
Motivation
  Growing needs for control and coordination of spatially distributed resources
  Communication network for information exchange
Notes:   Consensus + gradient
  Leader and follower
  Two-layer consensus

## Slide 3: Contents
Examples of US Distributed Control Programs
A Distributed Cooperative Power Allocation Method for Campus Buildings
Minimum-time Consensus Based Control and its Grid Applications
Transactive Control & Coordination: A Double-Auction Based Approach to Distributed Control and Decision-making

## Slide 4: Examples of US Distributed Control Programs

## Slide 5: CCSI leads the way to reliability, efficiency, and sustainability
CCSI benefits extend to all infrastructures:
A more reliable electricity system capable of integrating more renewables
Buildings that consume less energy and contribute to stability of the power grid
Safer and more sustainable transportation systems
More cost-effective operation of power grid, buildings, and transportation systems
Advanced controls designed to address complexity and variability allow use of all components of our energy infrastructure to their full potential. The result is a more reliable operation, as well as a more efficient and sustainable use of natural resources.

## Slide 6: GMLC: Control Theory
Develop new control solutions including topologies, algorithms and deployment strategies for transitioning the power grid to a state where a huge number of distributed energy resources are participating in grid control to enable the grid to operate with lean reserve margins. The theory effort will recognize the need to engage legacy control concepts and systems as we transition to more distributed control.
PoP: FY16/17/18
Budget: $6.5M
Labs: LANL, PNNL, ANL, INL, NREL, SNL, LLNL
Partners: Oncor Electric Delivery, PJM Interconnection LLC, United Technologies Research Center

## Slide 7: Virtual Battery-Based Characterization and Control of Flexible Building Loads Using VOLTTRON - Summary
FY16-17-18
$3.6M ($1.25M FY16)
Partners:
Target Market:
The solution is intended for deployment in commercial and residential buildings by energy service providers (e.g. utilities, aggregators) or control system vendors to provide transactive grid services
The goal of this project is to understand the capacity to use building loads as virtual storage resources and develop control methods to utilize that capacity for transactive buildings that provide grid services.
Understand the capacity of loads such as HVAC, hot water, and refrigeration in commercial and residential buildings to provide virtual storage as a substitute for physical storage on the power grid.
Develop algorithms to optimally control building loads to provide grid services and benefit building owners
Building Technologies Office

## Slide 8: Multi-scale Incentive-Based Control of Distributed Assets ARPA-E NODES
Incentive-based control provides stable response from millions of distributed assets
Available system flexibility estimated using simple virtual battery models
Incentive mechanisms used to economically and efficiently acquire resources without revealing private information
Engaged resources respond autonomously to self-sensed frequency and global control signal received from system
Technology Summary
Technology Impact
Improves efficiency and reliability of grid by engaging lowest cost resources to provide ancillary services
Provides level playing field for distributed assets with conventional generation sources
Reduces need for new transmission lines by providing fast-acting location-dependent resources
Proposed Technical Category and Target Metrics
Test Plan
A co-simulation platform will be designed spanning transmission, distribution, ancillary markets, and communication systems. Hardware-in-the loop will incorporate grid-edge control, DER equipment and systems coupled with virtual components in the simulation to address scalability. Incentive and control signals will be sent to the DER controllers of the HIL test systems. The physical responses of the devices are fed back into the simulation serving as feedback from the hardware to inform on the simulation.
Features | Description
Category | Category 1, 2 and 3
Managed DERs | residential and commercial HVAC systems, smart appliances, electric vehicles, thermal energy storage, PV inverters
FOA Metrics | Initial Response Time <2 seconds; reserve magnitude target >2% for frequency response, >5% for regulation, and >10% for ramping; availability >95%

## Slide 9: A Distributed Cooperative Power Allocation Method for Campus Buildings
He Hao, Yannan Sun, Thomas E. Carroll, and Abhishek Somani
Power & Energy Society General Meeting, 2015

## Slide 10: Background
5% peak reduction could reduce the wholesale electricity price by 50%
Peak shaving could save $10–15 billion/year for the U.S. electricity market
Buildings consume about 40% of energy and 75% of electricity in the U.S.
There are 5.6 million commercial buildings, contributing 1/3 of peak load
Peak demand is short, but contributes up to 50% of the overall building bill
Objective: design a distributed and scalable power allocation method for peak load management and other types of demand modulation for a campus with many buildings.

## Slide 11: Model Predictive Control approach to characterize building power flexibility

## Slide 12: Nash bargaining and dual decomposition are used to solve the negotiation problem
43 buildings

## Slide 13: Results
Model Predictive Control
MPC
Dual Decomposition
Nash Bargaining

## Slide 14: Distributed Control for Grid Applications

## Slide 15: Communication Network Effects – Traffic Congestion
Minimum-time Consensus and its grid applications
  T. Yang, D. Wu, Y. Sun and J. Lian, “Minimum-time consensus based approach for problems in a smart grid,” IEEE Transactions on Industrial Electronics, vol. 62, no. 12, pp. 1318-1328, 2016.

## Slide 16: Motivation
Classical consensus algorithm converges asymptotically
High communication cost
Time constraints
How to reduce the computational time?

## Slide 17: Minimum-time Consensus
Minimum-time consensus
  Each agent runs classical consensus and stores local states over a few number of time steps
  Computes the consensus value with local states within a minimum number of time steps even before consensus is achieved with a reasonable accuracy
  Accelerate the convergence time and alleviate the communication burden
Grid applications: Load shedding and economic dispatch problem

## Slide 18: Minimum-time Consensus
Step 1: each agent runs the classical consensus
Step 2: stores the local states, computes the differences, and constructs a square Hankel matrix
Step 3: check the rank, If it loses rank, then computes its normalized kernel
Step 4: computes the final consensus value

## Slide 19: Minimum-time Consensus Backup
Guaranteed to lose rank at time step
is equal to the degree of a minimal polynomial of the matrix pair
where
The minimal polynomial of the matrix pair denoted by
is the monic polynomial of the minimum
degree that satisfies

## Slide 20: Application to Distributed Load Shedding
Recall the ratio consensus based algorithm
It computes the average asymptotically in the sense that
Apply the minimum-time consensus, each agent computes the average system overload in a minimum number of time steps

## Slide 21: Case studies
IEEE 14-bus system
Communication network is the same as the physical topology
Figure: Discovery process using the existing algorithm vs our algorithm

## Slide 22: Case studies
Directed Communication network with the edge set
Figure: Discovery process using the existing algorithm vs our algorithm

## Slide 23: Application to EDP
Recall the distributed algorithm for EDP
It solves the EDP asymptotically
Apply the minimum-time consensus, EDP is solved in a minimum number of time steps

## Slide 24: Case studies
Directed communication network
Figure: Communication topology

## Slide 25: Case studies
Figure: Comparison of Incremental Cost Evolution Process

## Slide 26: Communication Network Effects – Directional Communication Links with Delays
Ratio consensus based control and its application to load shedding

## Slide 27: Classical Consensus Algorithm
Classical consensus algorithm
Let
Examples: sensor network, social opinion dynamics
Average consensus is achieved asymptotically, i.e.,
if and only if P is a primitive doubly stochastic matrix, or equivalently, the directed graph is strongly connected and balanced
In general, weighted average consensus is achieved

## Slide 28: Ratio Consensus Algorithm
How to compute the average for general directed graphs?
Ratio consensus algorithm
It computes the average asymptotically in the sense that

## Slide 29: Why Average?
P is column stochastic and primitive, according to the Perron-Frobenius Theorem,
where
is the normalized right eigenvector of

## Slide 30: Ratio Consensus Algorithm with Time Delays
Ratio consensus algorithm with bounded communication time delays
where
is an indicator function that captures the bounded delays
Robust to arbitrarily large but bounded communication time delays
Augmented digraph representation method

## Slide 31: Case Studies
A simple example with two nodes
Top figure – no delay
When the nodes experience bounded time-varying delays, we add “virtual” nodes
Middle figure – delays upper bounded by 2 time steps. Communication either directly or through the “virtual” nodes
Bottom figure – a particular scenario where

## Slide 32: Application to Load Shedding
When generation is insufficient to support all loads, effective load shedding needs to be deployed
Distributed algorithm for discovering the average system overload
Undirected communication networks without communication time delays
We propose a ratio consensus based distributed algorithm to discover the average system overload over directed communication networks even with arbitrarily large time varying delays

## Slide 33: Case Studies
IEEE 14-bus system
Communication network is independent of the physical topology and is modeled as a directed graph
with the node set V={1,2,….,14} and the edge set
The directed graph is strongly connected
However, not balanced since for node 2, the in-degree is
which is not equal to its out-degree

## Slide 34: Case Studies
Figure: Perfect communication

## Slide 35: Case Studies
Figure: Uniform constant delay equal to 3

## Slide 36: Case Studies
Figure: Time-varying delays
For time varying bounded 5 steps, both y and z do not converge, however, their ratio y/z converges to the average system overload.

## Slide 37: Impacts of Communication Networks on Distributed Controls
  Investigate the network effects on existing distributed control algorithms for grid applications
  Time delays
  Packet dropouts
  Directional communication links
  Develop distributed control algorithms to better accommodate various communication network effects
Objective

## Slide 38: Communication Network Effects – Time Delays
Impacts of communication time delays on distributed algorithms for EDP
  T. Yang, D. Wu, Y, Sun and J. Lian, “Impacts of time delays on distributed algorithms for economic dispatch,” in Proc. IEEE Power Energy Society General Meeting, Denver, CO, July 26-30, 2015.

## Slide 39: Distributed Algorithms for EDP
Economic Dispatch Problem (EDP)
Centralized vs. distributed
Several consensus-based distributed algorithms have been proposed.
In these algorithms, information is exchanged through a perfect communication network.
However, communication time delays are ubiquitous in network. We aim to investigate impacts of delays on a distributed algorithm.

## Slide 40: Consensus-based Distributed Algorithm w/o Time Delays
Quadratic cost function
For strongly connected communication networks

## Slide 41: Impacts of Communication Time Delays
Distributed algorithm with communication time delays

## Slide 42: Case Studies
Distributed algorithm with communication time delays
Figure: Communication topology
row stochastic
column stochastic

## Slide 43: Case Studies
Figure: Converge to the centralized optimal value

## Slide 44: Case Studies
Figure: Converge to the centralized optimal value yet with a slower convergence rate

## Slide 45: Case Studies
Figure: Diverge, power balance is not achieved

## Slide 46: Case Studies
Figure: Converge to the incorrect value, power balance is not achieved

## Slide 47: Case Studies
Figure: Converge to the incorrect value, more oscillation during the transient

## Slide 48: Conclusion and Future Work
Communication time delays have negative impacts
  Slower convergence rate
  Divergence
  Converge to incorrect values
Propose distributed algorithm for EDP to accommodate time delay impacts

## Slide 49: Conclusion and Future Work
A ratio consensus based distributed algorithm for load shedding over directed communication networks even with arbitrarily large time varying delays
Consider impacts of packet dropouts of the proposed algorithm

## Slide 50: Transactive Control & Coordination: A Double-Auction Based Approach to Distributed Control and Decision-making

## Slide 51: Transactive Cooling Thermostat Generates Demand Bid based on Customer Settings Price (Cooling Example) –
Thermostat (Today)
k
Tmax
Tmin
k
1
Indoor Temperature
Price*
Tcurrent
Pbid
Pavg
Pclear
Tset
Tdesired
User‘s comfort/savings setting implies limits around normal setpoint (Tdesired), temp. elasticity (k)
Current temperature used to generate bid price at which AC will “run”
AMI history can be used to estimate bid quantity (AC power)
Market sorts bids & quantities into demand curve, clears market returns clearing price
Thermostat adjusts setpoint to reflect clearing price & temperature elasticity
More
Comfort
More Savings
Translates to: k, Tmax, Tmin
Notes: AMI = advanced metering infrastructure

## Slide 52: RTP Double Auction Market – Uncongested
Pbase
Retail RTP based on wholesale real-time LMP (Base RTP)
Unresponsive
Loads
Q, Load (MW)
P, Price ($/MWh)
Responsive
Loads
Demand Curve: sorted (P, Q) bids from trans-active customers
Pclear =
Qclear
Feeder Capacity
Varies every TS = 5
min
Feeder Supply Curve
Market clears every TS= 5min (to ~match AC load cycle)
When uncongested:
  Quantity (Qclear) varies with demand curve
  Price (Pclear) is constant, equal to Base RTP
Qmin
Qmax
Market clears at intersection of supply & demand curves
Notes: RTP = real time pricing

## Slide 53: RTP Double Auction Market – Congested
Retail RTP based on wholesale real-time LMP (Base RTP)
Unresponsive
Loads
Q, Load (MW)
P, Price ($/MWh)
Responsive
Loads
Demand Curve: sorted (P, Q) bids from trans-active customers
Pclear
Qclear
Rated Feeder Capacity
When constrained:
  Quantity (Qclear) is constant at rated feeder capacity
  Price (Pclear) varies to keep load at rated capacity
Feeder Supply Curve
Pbase
Market clears at intersection of supply & demand curves
Qmin
Qmax

## Slide 54: What about the Congestion Surplus?
Feeder Supply Curve
customers providing capacity
Q, Load (MW)
P, Price ($/MWh)
Pclear
Qclear
Feeder Capacity
Congestion surplus is extra revenue collected from customers during constrained conditions (i.e. Pclear > Pbase)
Each customer’s surplus returned as billing rebate to maintain revenue neutrality
A PTR-like* incentive is also offered during congestion, based on customer’s bid history
Pbase
Congestion Surplust
Qbid
Pbid
* peak time rebate
Qtotal
congestion rebate
congestion incentive

## Slide 55: Hierarchical Network of Transactive Nodes Parallels the Grid Infrastructure
Node Functionality:
  “Contract” for power it needs from the nodes supplying it
  “Offer” power to the nodes it supplies
  Resolve price (or cost) & quantity through a price discovery process
  market clearing, for example
  Implement internal price- responsive controls
Node: point in the grid where flow of power needs to be managed

## Slide 56: Olympic Peninsula Demonstration
ancillary services
0 6 12 18 24
IBM
distribution congestion
transmission congestion
wholesale cost
Johnson Controls
Invensys
Johnson
Controls
$
MW
Market
Internet broadband
communications
Clallam PUD & Port Angeles
n = 112, 0.5 MW DR
Clallam County
PUD Water
Supply District
0.2 MW DR
Sequim Marine Sciences Lab
0.3 MW DR
0.5 MW DG

## Slide 57: Pacific Northwest Demonstration Project
What:
$178M, ARRA-funded, 5-year demonstration
60,000 metered customers in 5 states
Why:
Quantify costs and benefits
Develop communications protocol
Develop standards
Facilitate integration of wind and other renewables
Who:
Led by Battelle and partners including BPA, 11 utilities, 2 universities, and 5 vendors
Notes: 1 = PGE | 2 = Bonneville Power Administration | 3 = Peninsula Light Co. | 4 = Seattle City Light/University of Washington
5 = City of Ellensburg | 6 = Battelle | 7 = Benton PUD | 8 = Milton Freewater | 9 = Avista | 10 = Flathead Electric
11 = Northwestern Energy | 12 = Idaho Falls Power | 13 = Lower Valley Energy
57

## Slide 58
Thank you for your attention.
Any questions?